## Slide 1
INSTRUCTOR : FRED KAGAME
School Computing and IT
BIT,MSIT,CCNA,CCNP,CISA
ADVANCED NETWORKING

## Slide 2
Routing is the process of selecting the best path for data packets to travel from a source to a destination across interconnected networks. It ensures efficient, reliable, and secure communication in:
Local Area Networks (LANs)
Wide Area Networks (WANs)
The Internet (Global IP Routing)
Key Objectives of Routing:
✔ Connectivity – Ensures devices can communicate across networks.
✔ Efficiency – Chooses the fastest or least congested path.
✔ Scalability – Supports growing networks without performance loss.
✔ Fault Tolerance – Automatically reroutes traffic if a link fails.
INTRODUCTION TO ROUTING

## Slide 3
We will discuss various concepts and commands used for
routing, including:
How to configure a static route
Verifying routes
Configuring default routes for the devices, and much more

## Slide 4
IP Routing is a fundamental process in networking where routers determine the best path for data packets to travel across a network from the source to the destination. This process is defined by IP routes—entries that help routers make decisions on where to send packets based on their destination IP addresses.
1. What is an IP Route?
An IP route is a set of instructions that guides data packets toward their destination through a network.
Each IP route contains:
  Destination Network: Specifies the IP address range for which the route applies.
  Subnet Mask: Defines the range of addresses in the network.
  Next Hop: The IP address of the next router to which packets should be forwarded.
  Interface: Specifies which interface on the router will send the packet.
Routes are stored in a router’s routing table and can be either static (manually configured) or dynamic (learned via routing protocols like RIP, OSPF, or BGP).

## Slide 5
Types of IP Routes
Directly Connected Routes:
  These routes connect networks that are directly attached to a router’s physical or virtual interfaces.
  When a router interface is assigned an IP address within a specific subnet, it automatically considers that subnet a directly connected route.
  Example: If a router’s interface has an IP in the 192.168.1.0/24 network, it will treat this network as directly connected and add it to the routing table.
  Characteristics:
    Automatically added to the routing table when an interface is up.
    Requires no configuration or updates by an administrator.
    Fundamental for internal routing within local subnets

## Slide 6
2. Static Routes:
Manually configured routes by network administrators.
Useful for simple, predefined paths, or as backup routes if dynamic routes fail.
Example: ip route 10.0.2.0 255.255.255.0 192.168.1.1 tells the router that any packets destined for 10.0.2.0/24
should be sent to the next hop 192.168.1.1.
Characteristics:
  Reliable and predictable, as they don’t change unless manually updated.
  Require administrative updates if there are changes in the network topology.
  Ideal for small networks or specific, controlled paths.

## Slide 7
3. Dynamic Routes:
Routes that are automatically learned and updated by routing protocols like RIP, OSPF,EIGRP, and BGP.
These routes adjust to network changes, making them suitable for complex or larger networks.
Example: A router running OSPF will dynamically learn routes from other routers in the network, automatically adding and adjusting paths in its routing table.
Characteristics:
  Scalability: Handles large networks with frequent changes effectively.
  Adaptability: Automatically updates when network conditions change, such as a link failure.
  Commonly used in enterprise networks and the Internet, where automatic adjustment is essential.

## Slide 9
Administrative Distance
Administrative Distance or AD is a specific value used by routers to determine the best path when presented with more than one different route to a similar destination address from different routing protocols.
By default, a static route gets configured to use an AD of which means it is fully trustworthy. Administrative distance ranges from the value of 0 to 255, and the level of trustworthiness decreases as the value gets higher. That means a route with an Administrative Distance of 0 is unequivocally trusted, while 255 cannot be trusted at all. The administrative distance of 0 is only assigned to the connected route.

## Slide 10
Each type of route is assigned a different type of AD.
The following are the type of routes and the Administrative value assigned by default.
Direct connected route – Administrative Distance = 0
Static Route – Administrative Distance = 1
Enhanced Interior Gateway Routing Protocol summary route (EIGRIP) – Administrative Distance = 5
Exterior Border Gateway Protocol (eBGP) – Administrative Distance = 20
EIGRIP Internal – Administrative Distance = 90
Open Shortest Path Fist Protocol – Administrative Distance = 110
Intermediate System to Intermediate System Protocol (IS-IS) Administrative Distance = 115
Routing Information Protocol (RIP) – Administrative Distance = 120
Exterior Gateway Protocol (EGP) – Administrative Distance = 140
Internal Border Gateway Protocol (iBGP) (external) Administrative Distance = 200

## Slide 11
Dynamic Routing Protocols: 1. Enhanced Interior Gateway Routing Protocol (EIGRP)
Enhanced Interior Gateway Routing Protocol (EIGRP) is a Cisco-developed hybrid routing protocol combining features of distance-vector and link-state protocols. It is known for its fast convergence, scalability, and efficient resource utilization, making it a popular choice for enterprise networks.
Key Features of EIGRP
Fast Convergence:
  Quickly adapts to network changes by recalculating routes with minimal disruption.
DUAL Algorithm:
  Leverages the Diffusing Update Algorithm (DUAL) to calculate the best path and backup routes while avoiding routing loops.

## Slide 12
Support for VLSM and CIDR:
  Enables the use of Variable Length Subnet Masking (VLSM) and Classless Inter-Domain Routing (CIDR), optimizing IP address allocation.
Load Balancing:
  Offers both equal-cost and unequal-cost load balancing, allowing efficient distribution of traffic across multiple links.
Efficient Updates:
  Uses multicast and unicast updates, transmitting routing information only when topology changes occur, thereby reducing bandwidth consumption.

## Slide 13
Distance-Vector Routing Protocols
How they work:
  Each router periodically sends its entire routing table (vector of distances) to its neighbors only.
  Routers calculate routes based on hop count or distance metric.
  They have a more “tell my neighbor what I know” approach.
Examples:
RIP (Routing Information Protocol)
IGRP (Cisco proprietary, obsolete)
Link-State Routing Protocols
How they work:
  Each router builds a topology map of the entire network.
  Routers flood link-state advertisements (LSAs) throughout the network.
  Each router independently runs Dijkstra’s Shortest Path First (SPF) algorithm to compute the best paths.
Link-State vs Distance-Vector routing protocols.
Examples:
  OSPF (Open Shortest Path First)
  IS-IS

## Slide 14
Feature | Distance-Vector | Link-State
Knowledge of network | Knows only neighbor’s info (distance & direction) | Knows full network topology
Updates | Periodic full routing table updates to neighbors | Sends only LSAs (changes), flooded to all routers
Algorithm | Bellman-Ford | Dijkstra’s SPF (Shortest Path First)
Convergence | Slower, risk of loops (e.g., count-to-infinity) | Faster, loop-free once SPF runs
Scalability | Small networks (less resource use) | Large networks (needs more CPU & memory)
Examples | RIP, IGRP | OSPF, IS-IS
quick summary table of the main differences between Link-State and Distance-Vector routing protocols:

## Slide 15
Configuration of EIGRP
Here’s a simple EIGRP configuration guide for a Cisco router:
1. Enabling EIGRP
Access the global configuration mode and enable EIGRP with an Autonomous System (AS) number, which must match on all routers for them to communicate.
Router(config)# router eigrp <AS-number>
2. Advertising Networks
Define the networks that will participate in EIGRP. Only interfaces that match these networks will be part of the EIGRP process.
EIGRP will automatically calculate the best route for each subnet within these networks.
Router(config-router)# network <network-address> <wildcard-mask>
Example:
  To advertise network 192.168.1.0/24:
Router(config-router)# network 192.168.1.0 0.0.0.255

## Slide 16
Example Configuration
Imagine you have two routers (R1 and R2) with directly connected interfaces and IP addresses in the 10.1.1.0/24 and 10.2.2.0/24 networks.
On Router 1:
Router(config)# router eigrp 100
Router(config-router)# network 10.1.1.0 0.0.0.255
Router(config-router)# network 10.2.2.0 0.0.0.255
On Router 2:
Router(config)# router eigrp 100
Router(config-router)# network 10.1.1.0 0.0.0.255
Router(config-router)# network 10.2.2.0 0.0.0.255
Note: The AS number (100) must be the same on both routers for them to establish an EIGRP relationship.
Additional Configuration Options
Adjusting Hello and Hold Timers (to control neighbor discovery times):
Router(config-if)# ip hello-interval eigrp <AS-number> <seconds>
Router(config-if)# ip hold-time eigrp <AS-number> <seconds>
Unequal-Cost Load Balancing:
  Enable Variance to support unequal-cost load balancing.
Router(config-router)# variance <multiplier>
Verify the EIGRP Configuration
View the EIGRP Neighbor Table:
Router# show ip eigrp neighbors
View the EIGRP Routing Table:
Router# show ip route eigrp
View EIGRP Topology Information:
Router# show ip eigrp topology

## Slide 17
Open Shortest Path First (OSPF) is a widely used link-state routing protocol. Designed by the Internet Engineering Task Force (IETF), OSPF is an Interior Gateway Protocol (IGP), meaning it is used within a single autonomous system (AS). It is known for its fast convergence, hierarchical design, and ability to efficiently route data through large and complex networks.
Key Features of OSPF
Link-State Protocol: Each router maintains a map of the network, using link-state advertisements (LSAs) to share information and build a complete topology.
Dijkstra's Algorithm: OSPF uses the Dijkstra algorithm to calculate the shortest path tree for routing decisions.
Area-Based Structure: OSPF can divide networks into areas to simplify routing and reduce overhead.
Classless: Supports Variable Length Subnet Masking (VLSM), allowing for flexible subnetting.
Cost Metric: Routes are calculated based on cost, which is typically based on link bandwidth.
Efficient Convergence: OSPF has fast convergence due to its periodic hello messages and database synchronization.
Open Shortest Path First (OSPF)

## Slide 18
OSPF Network Types and Area Design
OSPF Areas:
  Backbone Area (Area 0): All other OSPF areas must connect to Area 0, which acts as the network’s backbone.
  Standard Areas: Regular areas that connect to the backbone area.
  Stub, Totally Stubby, and Not-So-Stubby Areas (NSSA): Special area types that restrict external routes to simplify routing tables and reduce overhead.
Router Types in OSPF:
Internal Router (IR): Routers within a single area.
Area Border Router (ABR): Routers that connect two or more areas, typically between Area 0 and a non-backbone area.
Autonomous System Boundary Router (ASBR): Routers that connect an OSPF network to an external network, like the Internet.

## Slide 19
OSPF Configuration
Here's a step-by-step guide for configuring OSPF on Cisco routers.
1. Enable OSPF
Access global configuration mode, enable OSPF with a chosen process ID (locally significant), and define the areas for each network.
Router(config)# router ospf <process-id>
2. Advertise Networks in OSPF
Define the networks and assign them to specific OSPF areas.
The wildcard mask (opposite of a subnet mask) is used to define the range of addresses in the network.
Router(config-router)# network <network-address> <wildcard-mask> area <area-id>
Example: To advertise the 192.168.1.0/24 network in Area 0:
Router(config-router)# network 192.168.1.0 0.0.0.255 area 0

## Slide 20
3. Assigning OSPF Cost Manually (Optional)
By default, OSPF calculates cost based on bandwidth, but you can manually set it if needed.
Router(config-if)# ip ospf cost <cost-value>
4. Configure OSPF Timers (Optional)
Dead Timer: How long OSPF waits to declare a neighbor down if it doesn't receive hello packets.
Hello Timer: How often OSPF sends hello packets to establish and maintain neighbor relationships.
Router(config-if)# ip ospf hello-interval <seconds>
Router(config-if)# ip ospf dead-interval <seconds>
5. Configure OSPF on Point-to-Point Links (Optional)
For specific network topologies, you may set the OSPF network type.
Router(config-if)# ip ospf network point-to-point

## Slide 21
Example OSPF Configuration
For a network with two routers (R1 and R2), each with interfaces in Area 0 and directly connected:
On Router 1:
Router(config)# router ospf 1
Router(config-router)# network 10.1.1.0 0.0.0.255 area 0
Router(config-router)# network 10.2.2.0 0.0.0.255 area 0
On Router 2:
Router(config)# router ospf 1
Router(config-router)# network 10.1.1.0 0.0.0.255 area 0
Router(config-router)# network 10.3.3.0 0.0.0.255 area 0
Verifying OSPF Configuration
View OSPF Neighbors:
Router# show ip ospf neighbor
View OSPF Routes:
Router# show ip route ospf
View OSPF Database:
Router# show ip ospf database

## Slide 22
Border Gateway Protocol (BGP) is the primary routing protocol used to exchange routing information across different autonomous systems (AS) on the Internet. BGP enables routers in different networks (often belonging to different organizations) to communicate and determine the best paths for data traffic across the Internet.
Key Features of BGP
Path Vector Protocol: BGP uses path vector mechanisms to share routes, providing the AS path for each route. This helps prevent routing loops.
Scalability: BGP is highly scalable and can manage complex routing in large networks like the Internet.
Policies and Path Control: BGP allows for advanced control over route selection through attributes (like AS-path, Next Hop, Local Preference, MED), making it highly customizable.
Slow Convergence: BGP is designed for stable connections and thus has slower convergence than interior gateway protocols like OSPF or EIGRP.
Border Gateway Protocol (BGP)

## Slide 23
Types of BGP
eBGP (External BGP):
  Used to exchange routing information between different ASes (external networks).
iBGP (Internal BGP):
  Used within a single AS to distribute BGP routes across routers in the same network.

## Slide 24
BGP Configuration
Here’s a simple guide to configure BGP on Cisco routers:
1. Define the BGP Process and Specify the AS
Start the BGP process by specifying your autonomous system number.
Router(config)# router bgp <AS-number>
2. Configure BGP Neighbors
BGP requires manual configuration of neighbors (also called peers).
For eBGP, neighbors are in a different AS. For iBGP, neighbors are in the same AS.
Router(config-router)# neighbor <neighbor-IP-address> remote-as <neighbor-AS-number>
3. Advertising Networks in BGP
Specify which networks to advertise. For BGP, you should specify exact routes that exist in the router’s routing table.
Router(config-router)# network <network-address> mask <subnet-mask>

## Slide 25
Example BGP Configuration
Let’s say we have two routers, R1 and R2, in different autonomous systems (AS 100 and AS 200):
On Router 1 (AS 100):
Router(config)# router bgp 100
Router(config)# bgp router-ID 10.10.10.10
Router(config-router)# neighbor 192.168.2.2 remote-as 200
Router(config-router)# network 10.1.1.0 mask 255.255.255.0
On Router 2 (AS 200):
Router(config)# router bgp 200
Router(config-router)# neighbor 192.168.2.1 remote-as 100
Router(config-router)# network 10.2.2.0 mask 255.255.255.0
In this example:
R1 advertises the 10.1.1.0/24 network to R2.
R2 advertises the 10.2.2.0/24 network to R1.

## Slide 26: Thank you for your support and dedication throughout this module! Your commitment and engagement made it an enjoyable and rewarding experience.
We wish you all the very best in your future endeavors